## Slide 1: Estimation of DC Motor Load
Project Members: Marco Menchetti, Adrija Sen, Andrea Malaguti
Guided By: Prof. Claudia Califano
Course: Digital Systems Control

## Slide 2
Goal of the project :
Estimation of DC Motor parameters
Estimation of DC Motor load
Estimation of a PI Controller

## Slide 3
HARDWARE AND SOFTWARE USED:
Arduino Uno R3
DC Motor (2x12V)
H-Bridge(LM298-N)
Hall-Effect Encoder
Operational Amplifier(LM324N)
Resistors()
Potentiometer 1KΩ
Power Supply – (12V, 2A max.)
Matlab 2019a
Matlab Arduino support package

## Slide 4
Arduino UNO R3

## Slide 5
Arduino Uno is a microcontroller board based on the ATmega328P (datasheet). It has 14 digital input/output pins (of which 6 can be used as PWM outputs), 6 analog inputs, a 16 MHz quartz crystal.
Tech Specifications of Arduino UNO R3:
Operating Voltage | 5V
Input Voltage (recommended) | 7-12V
Input Voltage (limit) | 6-20V
Digital I/O Pins | 14 (of which 6 provide PWM output)
PWM Digital I/O Pins | 6
Analog Input Pins | 6
DC Current per I/O Pin | 20 mA
DC Current for 3.3V Pin | 50 mA
Flash Memory | 32 KB (ATmega328P) of which 0.5 KB used by bootloader
SRAM | 2 KB (ATmega328P)
EEPROM | 1 KB (ATmega328P)
Clock Speed | 16 MHz
LED_BUILTIN | 13

## Slide 6
DC Motor + Encoder

## Slide 7: TECHNICAL SPECIFICATIONS FOR ENCODER-MOTOR DUO
Operating voltage: 6V to 18V
Rated voltage: 12V
Reduction ratio: 40:1
No-load current: 40 mA
No-load speed: 150 RPM
Rated torque: 1.5 kg cm
Maximum torque: 6.4 kg cm
Stop current: 1.3 A
Hall Incremental Encoder
Encoder resolution: 440 CPR
Weight: 150 g
Red: Motor power +
Black: Encoder GND
Green: Encoder Phase A
Yellow: Encoder Phase B
Blue: Encoder power supply 5V
White: Motor power

## Slide 8: LM324N (OPERATIONAL AMPLIFIER)
Pin-out for LM324N
Slew Rate | 0.5V/µs | 
Gain Bandwidth Product | 1,2MHz | 
Current - Input Bias | 20nA | 
Voltage - Input Offset | 3mV | 
Current - Supply | 1.4mA | 
Current - Output / Channel | 40mA | 
Voltage - Supply, Single/Dual (±) | 3V ~ 32V, ±1.5V ~ 16V | 
Operating Temperature | 0°C ~ 70°C | 

## Slide 9: LM324N-NON-INVERTING AMPLIFIER
The gain of the non-inverting op-amp is calculated as:
We took the value of the resistors as :
R2= Ω
R1= Ω
Therefore, the gain Av=

## Slide 10: L298N (H-BRIDGE DRIVER)

## Slide 11: L298N (TECHNICAL SPECIFICATIONS )
Technical | 
Bandwidth | 1 MHz
Common Mode Rejection Ratio | 70 dB
Dual Supply Voltage | 9 V
Gain | 100 dB
Gain Bandwidth Product | 1.3 MHz
Input Bias Current | 150 nA
Input Offset Voltage (Vos) | 7 mV
Max Dual Supply Voltage | 15 V
Max Operating Temperature | 70 °C
Max Supply Voltage | 30 V
Min Dual Supply Voltage | 1.5 V
Min Operating Temperature | 0 °C
Min Supply Voltage | 3 V
Nominal Supply Current | 1.2 mA
Number of Amplifiers | 4
Number of Channels | 4
Number of Circuits | 4
Number of Elements | 4
Operating Supply Current | 1.5 mA
Operating Supply Voltage | 15 V
Output Current | 70 mA
Output Current per Channel | 70 mA
Slew Rate | 0.4 V/µs
Voltage Gain | 100 dB

## Slide 12: PULSE WIDTH MODULATION
Pulse Width Modulation(PWM) allows us to vary how much time the signal is high in an analog fashion. While the signal can only be high (usually 5V) or low (ground) at any time, we can change the proportion of time the signal is high compared to when it is low over a consistent time interval.

## Slide 13
Sample output of PWM modulated signal
d=
Type equation here.
Duty Cycle is given by:

## Slide 14: INCREMENTAL ENCODERS
An incremental encoder generates a pulse for each incremental step in it's rotation. The most common type of incremental encoder uses two output channels (A and B) to sense position. Using two code tracks with sectors positioned 90° out of phase, the two output channels of the quadrature encoder indicate both position and direction of rotation. If A leads B, for example, the disk is rotating in a clockwise direction else vice versa.

## Slide 15: Motor Parameters Estimation
Since,
Therefore,
ω: rated speed
J: motor inertia
B: friction
Ra: armature resistance
ia: armature current
Eemf: back-ElectroMotiveForce

## Slide 16
Where, Vs= 12 V
ia = 40 mA (rated)
Ra= 13.7 Ω (estimated)
ω = 150 RPM = 15,7 rad/s
Back-EMF constant and Torque constant have the same numerical value for DC motors:
So,
&

## Slide 17: MECHANICAL TIME CONSTANT ESTIMATION
Mechanical time constant:
Time needed by the angular velocity to reach 63% of final value.
Gives us,
J=
=40ms
Now using, =

## Slide 18: LOAD TORQUE ESTIMATION
Inserting B=0, we get,
Also at steady state, =0. Therefore, =0.
This gives, .
We know , T
Torque-Current relationship

## Slide 19: CONCLUSIONS
During the development of this project we have learnt the following:
Learned how to interface Arduino and Matlab for real time
simulation and analysis
Estimated the DC motor parameters in order to obtain an estimate
of the motor torque
Implemented a PI speed controller and seen the effects of the
proportional and integral gains.
Future work: possibly, an implementation of a position controller
introducing external sensors to create a zero reference signal
(mechanical or magnetic switch).