Estimation of DC motor load
Team: Alessia De Matteis, Andrea Guidi, Manuel Donsante
Course: Digital Control Systems
Academic Year: 2017/2018

---
Objectives
Estimation of DC motor parameters
Design of a PI speed regulator
2/27/18
Page 2

---
Page 3

---
Hardware and software
- Arduino Due (ARM Cortex-M3 CPU)
- 2x 12V DC Motor
- Hall Effect Encoder
- H-bridge: L298-N
- Operational Amplifier: LM324N
- 1KΩ Potentiometer
- Resistors: 2x 12KΩ, 2x 33KΩ, 1x 1Ω
- 12 V Power Supply – 20 A max
- MATLAB 2017b
- MATLAB Arduino support package
- Fritzing
Page 4

---
Hardware: Arduino Due
The Arduino Due is a microcontroller board based on the
Atmel SAM3X8E ARM Cortex-M3CPU.
It has 54 digital input/output pins (of which 12 can be used as PWM outputs) and 12 analog inputs.
Used to drive the motor by the H-bridge, to read the voltage from the potentiometer and to read the digital signal from the encoder.
Page 5

---
Hardware: DC Motors + Encoders
Operating voltage: 6V to 18V
Rated voltage: 12V
Reduction ratio: 40:1
No-load current: 40 mA
No-load speed: 150 RPM
Rated torque: 1.5 kg cm
Maximum torque: 6.4 kg cm
Stop current: 1.3 A
Hall Incremental Encoder
Encoder resolution: 440 CPR
Weight: 150 g
Red: Motor power +
Black: Encoder GND
Green: Encoder Phase A
Yellow: Encoder Phase B
Blue: Encoder power supply 5V
White: Motor power -
Page 6

---
Incremental Encoders
Incremental encoders can measure relative displacements starting from an arbitrary position.
They use two digital outputs, A and B phases, set in quadrature.
B phase is commonly used for detecting sense of rotation.
MCUs generally use software interrupts for phase detection and counters to measure increments in position.
Page 7

---
Hardware: L298-N and LM324N
The L298-N
Is a dual full-bridge driver capable of driving inductive loads such as motors
Can supply up to 2A per motor.
Has logic pins to allow to enable or disable motors (or speed regulation with PWM)
A pin for the connection of an external sensing resistor is available; (for this purpose,
a 1Ω resistor was connected to this pin)
The LM324N
Is a quad operational amplifier used for example as a DC gain block (as in our case).
Can operate from a single supply over a wide range of voltages.
It was used to amplify the voltage signal from the current sensing resistor on L298-N.
Page 8

---
PWM (Pulse Width Modulation)
Pulse Width Modulation (PWM) is a technique of modulation of a digital signal.
It is based on generating a square wave with fixed frequency but variable duty cycle d.
It can be used to drive power systems without affecting performances (such as DC motors).
Duty cycle:
Page 9
d=\frac{T_{on}}{T}

---
Non-inverting Amplifier LM324N
Rf = Rg = 33 KΩ have been chosen in such a way that G=2.
Page 10
G = 1+ \frac{R_f}{R_g}

---
Wiring diagram
Page 11

---
Motor parameters estimation
Motor dynamical equations:
ω, rated speed
J, motor inertia
B, friction
Ra, armature resistance
ia, armature current
Eemf, back-ElectroMotiveForce
Back-EMF constant:
Page
\begin{cases} T - T_L = J \frac{d\omega}{dt} + B \omega \\ V_s = E_{emf} + R_a i_a \end{cases}
E_{emf} = K_e \omega V_s = K_e \omega + R_a i_a
K_e = \frac{V_s - R_a i_a}{w}

---
Motor parameters estimation
Where Vs= 12 V
      ia = 40 mA (rated)
      Ra= 13.7 Ω (estimated)
ω = 150 RPM = 15,7 rad/s
Back-EMF constant and Torque constant have the same numerical value for DC motors:
So,
Page 13
K_e \left[ \frac{V}{rad/s} \right]= K_T \left[\frac{Nm}{A} \right]
K_T = 0.729 \, \left[ \frac{N \, m}{A}\right]
K_e = \frac{V_s - R_a i_a}{w}= 0.729 \left[ \frac{V }{rad/s} \right]

---
Mechanical time constant estimation
Mechanical time constant:
Time needed by the angular velocity
to reach 63% of final value.
We can compute motor inertia:
Page 14
J = \frac{K_e K_T \tau_{mech}}{R_a} \ [kg \, m^2]
J = 2 \cdot 10^{-3} \ \left[ kg \, m^2 \right]
\tau_{mech} = \frac{R_aJ}{K_e K_T} \ [s]
Using:
\tau_{mech} = 55 \ \left[ ms \right]

---
Load torque estimation
Motor dynamical equations:
Neglecting friction:
At steady state:
Torque – current relationship
We finally know that:
Page 15
B = 0
J \frac{d \omega}{dt} = 0
T-T_L = J \frac{d \omega}{d t }
T = T_L
T = K_T i_a
\begin{cases} T - T_L = J \frac{d\omega}{dt} + B \omega \\ V_s = E_{emf} + R_a i_a \end{cases}

---
Matlab code: Motor Load Estimation
Page 16

---
Matlab code: Motor Load Estimation
Page 17

---
Motor Load estimation: a video
Page 18

---
Matlab code: P/PI Speed Controller
Page 19

---
Matlab code: P/PI Speed Controller
Page 20

---
Simulation: P vs PI Controller
Page 21

---
PI controller: a video
Page 22

---
Conclusions
During the development of this project we have:
Learned how to interface Arduino and Matlab for real time simulation and analysis;
Estimated the DC motor parameters in order to obtain an estimate of the motor torque;
Implemented a PI speed controller and seen the effects of the proportional and integral gains.
Future work: possibly, an implementation of a position controller introducing external sensors to create a zero reference signal (mechanical or magnetic switch).
Page 23